## Slide 1: Material and Cross-section properties
BOA001
Ing. Martin Vild, Ph.D.
9/2024

## Slide 2: Presenting
Ing. Martin Vild, Ph.D.
IDEA StatiCa – Product Owner
FCE BUT – Assistant professor
Research:
Steel connections
Finite element analysis
Scopus Author ID: 56188615700
Committee member:
CEN/TC 250/SC 3/WG 8 "Evolution of EN 1993-1-8 - Joints and connections“
ECCS TC10 “Structural Connections”
Website:
https://www.fce.vutbr.cz/KDK/vild.m/
email: martin.vild@vutbr.cz
Office: C203
Consultations:
Thursday 10–11

## Slide 3: Content
Repetition makes masters
  Snow load “+” Wind load “+” Dead load
Material
  Steel
  Timber
Connections
  Bolts
  Welds
Member design
  Tension/Compression
  Bending
  Shear
  Torsion
Concrete vs Steel, which material to use?

## Slide 4: Load combination
kN/m2
kN/m2
kN/m2
kN/m2
Snow
Wind

## Slide 5: Load combination
EN 1990, comb. 6.10
kN/m2
kN/m2
kN/m2
kN/m2
kN/m2

## Slide 6: Load combination
Compression:
Suction:

## Slide 7: Material – Steel
EN 1993
https://material-properties.org/what-is-ultimate-tensile-strength-uts-definition/

## Slide 8: Material – Timber
EN 1995
Orthotropic
Many types:
  Solid timber
  Glued lamilated timber
  LVL, plywood, OSB
  Particleboard, Fibreboard

## Slide 9: Material properties
 | Steel S355 | Timber C24 | Concrete C20/25
Bulk density | 7850 kg/m3 | 420 kg/m3 | 2400 kg/m3
Poisson’s ratio | 0.3 | ~0.3 | 0.2
Modulus of elasticity | 210 000 MPa | 11 000 MPa | 30 000 MPa
Shear modulus | 80 769 MPa | 690 MPa | 12 500 MPa
Safety factor | 1.0 | 1.3 | 1.5
Characteristic strength | 355 MPa | 24 MPa | 20 MPa
Design strength | 355 MPa | 11.1 MPa | 13.3 MPa
 | Steel S355 | Timber C24 | Concrete C20/25
 | 7850 kg/m3 | 420 kg/m3 | 2400 kg/m3
 | 0.3 | ~0.3 | 0.2
 | 210 000 MPa | 11 000 MPa | 30 000 MPa
 | 80 769 MPa | 690 MPa | 12 500 MPa
 | 1.0 | 1.3 | 1.5
 | 355 MPa | 24 MPa | 20 MPa
 | 355 MPa | 11.1 MPa | 13.3 MPa

## Slide 10: Connections – Bolts
Material: ISO 898-1
Sizes: ISO 4014
https://www.orbitalfasteners.co.uk/
Chart: ε [-]
| 0 | 0.4627857142857143 | 0.4667857142857143 | 1.1797857142857142 | 1.8887857142857143 | 2.5917857142857144 | 3.2897857142857143 | 3.9837857142857143 | 4.6727857142857143 | 5.3567857142857145 | 10
Bolt 10.9 | 0 | 971.85 | 971.89 | 1012.91 | 1044.68 | 1068.65 | 1086.27 | 1099.07 | 1108.61 | 1116.5 | 1150
S235 | 0 | 298.6782 | 299.1647 | 380 | 470 | 516 | 549.2166
Bolt grade | [MPa] | [MPa]
4.6 | 240 | 400
4.8 | 320 | 400
5.6 | 300 | 500
5.8 | 400 | 500
6.8 | 480 | 600
8.8 | 640 | 800
10.9 | 900 | 1000
Bolt grade |  | 
4.6 | 240 | 400
4.8 | 320 | 400
5.6 | 300 | 500
5.8 | 400 | 500
6.8 | 480 | 600
8.8 | 640 | 800
10.9 | 900 | 1000

## Slide 11
Kovozoo, Staré Město

## Slide 13: Connections – Welds
https://northern-weldarc.com/types-welding-processes/
https://www.twi-global.com/technical-knowledge/faqs/what-is-welding

## Slide 14: Stresses

## Slide 15: von Mises stress
https://en.wikipedia.org/wiki/Von_Mises_yield_criterion

## Slide 16: von Mises stress
Impact on member design:
Normal stress
  Tension & compression:
  Bending:
Shear
Combination:
for
Chart: VEd/Vpl,Rd
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.52 | 0.54 | 0.56000000000000005 | 0.57999999999999996 | 0.6 | 0.62 | 0.64 | 0.66 | 0.68 | 0.7 | 0.72 | 0.74 | 0.76 | 0.78 | 0.8 | 0.82 | 0.84 | 0.86 | 0.88 | 0.9 | 0.92 | 0.94 | 0.96 | 0.98 | 1
 | 1 | 1 | 1 | 1 | 1 | 1 | 0.9984 | 0.9936 | 0.9856 | 0.9744 | 0.96 | 0.9424 | 0.9216 | 0.8976 | 0.8704 | 0.84 | 0.8064 | 0.7696 | 0.7296 | 0.6864 | 0.64 | 0.5904 | 0.5376 | 0.4816 | 0.4224 | 0.36 | 0.2944 | 0.2256 | 0.1536 | 0.0784 | 0

## Slide 17: Tension & Compression
Integral
Discrete

## Slide 18: Example
Calculate area of cross-section HEB 500
Calculate tensile resistance of HEB 500
h = 500 mm
b = 300 mm
tf = 28 mm
tw = 14.5 mm
r1 = 27 mm
d = 390 mm
Roughly (5 minutes)
Exactly (who has time)
http://www.staticstools.eu/cs/profile-heb/HE500B/mm/show

## Slide 19: Bending – stiffness

## Slide 20: Bending – resistance

## Slide 21: Shear
Simplified:

## Slide 22: Shear area

## Slide 23: Torsion
Saint Venant torsion
Warping

## Slide 24: Cross-section properties – Table
http://www.staticstools.eu/cs/

## Slide 25: Center of gravity

## Slide 26: Example
Calculate:
Area [mm2]
Normal resistance [N]
Center of gravity
Moment of inertia:
Beam deflection:
Section modulus:
Moment resistance:
,
80
80
80
80
200
[mm]
kN/m
kN/m