## Slide 1: Modelování kovových a dřevěných konstrukcí
NOB021
doc. Ing. Martin Vild, Ph.D.
4/2026

## Slide 2: Prezentuje
doc. Ing. Martin Vild, Ph.D.
IDEA StatiCa – Product Owner
VUT FAST – Docent
Výzkum:
Přípoje ocelových konstrukcí
Metoda konečných prvků
Scopus Author ID: 56188615700
Člen komisí:
CEN/TC 250/SC 3/WG 8 "Evolution of EN 1993-1-8 - Joints and connections“
ECCS TC10 “Structural Connections”
Web:
https://www.fce.vutbr.cz/KDK/vild.m/
email: martin.vild@vutbr.cz
Kancelář: C203

## Slide 3: Eurocode – verbal forms
Shall = obligatory
Should = highly recommended
May = permitted
Can = a possibility

## Slide 4
Eurocode – verbal forms

## Slide 5
Eurocode – verbal forms
As an engineer, I get to choose (unless the investor or peer reviewer says otherwise).
Formula
FEA
Experiments
EC acceptance
Cost
Time
Accuracy

## Slide 6: Design using experiments
Code clauses are designed to be:
  Safe
  Simple
Engineering judgement is needed
  Safe assumptions
Experiments are useful when design is repeated
  Thin-walled purlins (Voestalpine)
  Anchors (Hilti, Fisher)
  Prefabs (Prefa kompozity)

## Slide 7: Research centers
Not so many of them
Certification, calibration
Expensive equipment
Skilled staff
Leads to much better understanding

## Slide 9: EN 1990 – Reliability

## Slide 10: EN 1990 – Distribution functions

## Slide 11: Pilot test
Fabrication of specimens
Failure modes
Manufacturing tolerances
Loading – displacement/force controlled, speed
Measure at what frequency and accuracy
Can I evaluate everything?

## Slide 12: EN 1990 – Annex D
known:
  Literature
  Previous tests
  Plate / weld / bolt alone
unknown:
  Combined failures
 | Plate () | Weld ( | Bolt ()
 | 0.07–0.10 | 0.10–0.15 | 0.05–0.08
 | 0.07–0.10 | 0.10–0.15 | 0.05–0.08

## Slide 13: EN 1990 – Annex D
Correction factor:
Does the experiment correspond to the reality?
  Temperature (–60 °C – brittle)
  Loading rate, duration (glues – creep)
  Humidity (timber)
  Volume, scale effects
  ...
In practice steel joints

## Slide 14: EN 1990 – Annex D
Average value :
When all experiments are the same
If scale is different, consider scaling (e.g. , )

## Slide 15: EN 1990 – Annex D
Excel:
=STDEV.S(range) / AVERAGE(range)

## Slide 16: Task No. 1
Determine design resistance using experiments for bolts M16 10.9.
Steps:
For all bolts:
  Calculate for tensile resistance – becomes known
  Calculate for net diameter
  Compare to for tensile resistance
Calculate for M16 10.9
  Is it higher than design resistance in EN 1993-1-8?

## Slide 17: Task No. 2
Assess the reliability of tensile resistance of all bolts for design tensile resistance in EN 1993-1-8
Steps:
Create reliability graph ( on y-axis, on x-axis)
Calculate bias
Calculate
Assume
Calculate